A little about me

---
What will we do today?
This! (hopefully)
https://github.com/xansmolzy/Fri3d-KiCad101

---
Why KiCad?
- KiCad
  - Free and open source
  - Not too many features
  - Plugins
  - Mature software
  - Good backing and support

---
Workshop
- Start with schematic
- We will make an LED gadget
  - ESP32
  - WS2812B
  - USB-C
  - Sensors
Schematic
PCB manufacturer rules
PCB layout
Design rule checks
Manufacturing

---
Workshop
- Download template project
  - Add a schema page
  - Add LED
  - Add to main schematic
  - Add sensor to main schema

---
Schematic tips
- Reads like test, from left to right
  - Inputs on the left
  - Outputs on the right
- Reuse blocks for repetitive items
  - Brings structure
- Text annotations and rectangles help
  - Makes it easier to understand
  - Makes it more organized

---
Manufacturing rules
- Few options
  - Aisler
  - JLCPCB
  - PCBWay
  - Eurocircuits
  - ...

---
Manufacturing rules
- Look up rules
  - Aisler for example
    - Via size most important
    - Track spacing
    - KiCad default rules are good for most 2L boards

---
Layout tips (power)
- Capacitors go close to device
  - Good decoupling
- Use via stitching on large PCB
  - Ensure good ground connection over entire PCB
- Use power & ground planes
  - Make a very strong connection to power pins

---
Layout tips (thermal)
- Use lots of vias to sink heat away
  - If component expected to be hot
- Always use ground plane for PCB
  - Helps with heat

---
Layout tips (sensitive signals)
- Use ground plane for shielding
- Minimize wire crossings, cross at 90° if possible
  - Minimize crosstalk

---
Layout tips (manufacturing)
- Rounded PCB corners decrease risk of delamination
- Set good design rules
- Use ground planes to fill copper
  - Improves copper uniformity

---
DRC checks
- Check that PCB adheres to design rules
  - Checks that manufacturing is possible
  - Does some additional checks, like accidental shorts

---
- Export gerber files
  - Submit .zip to manufacturer
- Choose manufacturing options